## Slide 1
MPO
MPO
Pipeline
Reports
Architecture
-

## Slide 2
MPO PROJECT OVERVIEW
MPO
Pipeline
Reports
Architecture
The Website centralizes manufacturing performance data into one web-based reporting workspace. It addresses the operational bottleneck of reviewing production output, equipment stops, and pick-and-placement quality across multiple screens, manual data extracts, or disconnected records.
The project gives supervisors and management a faster path from MES production data to operational insight. Users can review line-level performance, identify recurring feeder or nozzle issues, assess downtime categories, and export filtered results for follow-up analysis.

## Slide 3
MPO
Pipeline
Reports
Architecture
BUSINESS VALUE
Improve Performance:
Reduces manual consolidation of production and quality data.
Improved Efficiency:
Helps teams focus corrective action on the highest-impact equipment and quality losses.
Flexible Reporting Filters
Creates a consistent, filterable view of performance by line, machine, model, part, feeder, and nozzle.
Export Excel
Supports management reporting through Excel export.

## Slide 4
Feature | What it does | Business Benefit
Overall Dashboard | Presents board production, top problematic feeders, top problematic nozzles, pickup/placement totals, PPM, and error-stop time by line. | Gives leadership an immediate operational health check and highlights where attention is needed.
Board Count DashboardBoard Count Dashboard | Visualizes production-board counts by selected line, lane, time range, and model. | Makes output trends easier to compare across lines and shifts.
Production Report | Lists produced panel and pattern quantities by line, lane, model, group, and time range. | Supports production tracking and provides a clear record of completed output.
MPO
Pipeline
Reports
Architecture
Slide 04
MPO
Project
KEY FEATURES AND VALUE

## Slide 5
MPO
Pipeline
Reports
Architecture
Slide 05
MPO
Project
END-TO-END DATA PIPELINE
LNB machines generate raw .u01 files. Files move through SFTP to the incoming folder, where Node-RED detects, reads, parses, and prepares them for PostgreSQL. The web application then turns the stored data into dashboards and reports.

## Slide 6
MPO
Pipeline
Reports
Architecture
Slide 06
MPO
Project
NODE-RED DATA PROCESSING
Node-RED extracts machine identity, MJS ID, lot, product, production counters, downtime, feeder data, and nozzle data. It calculates the delta between the current and prior counters, including counter-reset handling, before submitting one structured JSON payload to PostgreSQL.

## Slide 7
Slide 07
DATABASE DESIGN
MPO
Pipeline
Reports
Architecture
MPO
Project
PostgreSQL separates master machine data, historical production reports, feeder details, nozzle details, and the latest machine counter state. This structure supports efficient reporting while preserving the raw state required for accurate delta calculation after Node-RED restarts.

## Slide 8
MPO
Pipeline
Reports
Architecture
Slide 07
MPO
Project
REPORTING AND DRILL-DOWN
Management starts with the Overall Dashboard, then drills into Board Count, Production, Pick-Placement by Part, Feeder, Nozzle, Cycle Time, Downtime, and Total Pickup Placement reports. Each report supports filtering, pagination, adjustable columns, and Excel export.

## Slide 9
MPO
Pipeline
Reports
Architecture
Slide 09
MPO
Project
TECHNICAL ARCHITECTURE
The reporting application uses ASP.NET Core MVC on .NET 9 with C#, Entity Framework Core, Npgsql, PostgreSQL, Razor Views, Bootstrap, JavaScript, Chart.js, and Lucide icons. Backend and frontend components run in Docker containers.

## Slide 10
MPO
Pipeline
Reports
Architecture
Slide 10
MPO
Project
MPO FOR MANAGEMENT
MPO provides a single route from machine data to operational insight. During a live review, select the time period, review output and risks on the dashboard, drill into downtime or equipment detail, and export the exact filtered evidence for follow-up.
Manufacturing Performance Overview
LNB -> SFTP -> Node-RED -> PostgreSQL -> Docker Web Portal
-