## Slide 1
MANUFACTURING PERFORMANCE OVERVIEW
MPO
Machine Data → Performance → Action
Centralized production reporting for management, engineering, and maintenance.
LNB • SFTP • Node-RED • PostgreSQL • ASP.NET Core • Docker
PROJECT PROCESS & DESIGN OVERVIEW
PANASONIC • 01
Notes: MPO is a web-based manufacturing performance reporting system that turns raw LNB machine data into dashboards and reports for daily operations.

## Slide 2
EXECUTIVE SUMMARY
MPO Turns Machine Data into Action
MPO | Manufacturing Performance Overview
PANASONIC • 02
One automated flow unifies output, quality, and downtime—from .u01 files to the management dashboard.
01
Centralize
One unified reporting source for LNB machine data.
02
Analyze
Drill down by line, lane, machine, model, part, feeder, and nozzle.
03
Act
Identify at-risk equipment, investigate root causes, and export data.
Outcome: raw data becomes evidence for daily operations.
Notes: The dashboard highlights areas that need attention; detailed reports provide evidence for investigation.

## Slide 3
BUSINESS VALUE
Four Direct Operational Benefits
MPO | Manufacturing Performance Overview
PANASONIC • 03
01
One Data Source
Centralize production, quality, and downtime.
02
Reduce Manual Work
Eliminate multiple consolidation and file-reconciliation steps.
03
Faster Root-Cause Analysis
Trace issues from line to feeder, nozzle, or part.
04
Flexible Sharing
Export filtered results in an Excel-compatible format.

## Slide 4
SYSTEM AT A GLANCE
One Architecture, One Data Flow
MPO | Manufacturing Performance Overview
PANASONIC • 04
01
LNB
.u01 raw data
02
SFTP
Secure transfer
03
Node-RED
Parse + delta
04
PostgreSQL
Store + state
05
Web MPO
Dashboard + export
AUTOMATED
No manual file handling is needed after data enters PostgreSQL.
Notes: Overall flow: LNB raw data, SFTP, incoming folder, Node-RED Watch, parsing and delta calculation, PostgreSQL, ASP.NET Core, and the web frontend in Docker.

## Slide 5
MPO | Manufacturing Performance Overview
PANASONIC • 05
01
DATA PIPELINE
How MPO ingests, standardizes, and preserves cumulative counter meaning.
From Raw Data to Operational Decisions

## Slide 6
END-TO-END FLOW
Automated Data Flow in 8 Steps
MPO | Manufacturing Performance Overview
PANASONIC • 06
01
LNB Generates File
.u01 counters
02
SFTP Transfers File
incoming folder
03
Watch Detects File
filter valid files
04
Parse Content
machine + report
05
Calculate Delta
count + time
06
Write to Database
stored procedure
07
Restore State
after restart
08
Display on Web
dashboard + export
Critical control: delta counters + state persistence.
Notes: The entire process is automated, from raw files to reports. After data is stored in PostgreSQL, users work directly through the web dashboard.

## Slide 7
INGESTION & PARSING
Node-RED Standardizes .u01 Files
MPO | Manufacturing Performance Overview
PANASONIC • 07
01
Machine identity
Line • machine • lane • stage • type • version
02
Production context
MJS ID • lot • product • report date • output
03
Operational counters
Cycle time • production • downtime • error counters
MountPickupFeeder
→ feeder list by part, address, reel, and miss counters
MountPickupNozzle
→ nozzle list by head, address, name, and miss counters

## Slide 8
CORE PROCESSING LOGIC
Delta Counters Preserve Actual Output
MPO | Manufacturing Performance Overview
PANASONIC • 08
DELTA
= Current counter − Previous counter
Applied to
Production • Time • Feeder • Nozzle
First Reading
Delta = Current
No previous state
Normal
Delta = Current − Previous
Record only the increment
Counter reset
Delta = Current
Current < Previous
Prevent double counting • Handle machine resets • Maintain period accuracy
Notes: This is the most important point in the flow. Machines send cumulative values, while the system needs the actual increment for each period. Delta calculation prevents double counting and handles counter resets.

## Slide 9
EQUIPMENT-LEVEL DATA
Equipment Details Also Use Delta
MPO | Manufacturing Performance Overview
PANASONIC • 09
F
Feeder delta
Pickup, mount, and miss groups by feeder / slot / part.
N
Nozzle delta
Pickup, mount, and miss groups by nozzle / head.
Unified JSON payload → report_data + feeder_data + nozzle_data + raw_state

## Slide 10
STATE RECOVERY
Restart Does Not Lose Delta Context
MPO | Manufacturing Performance Overview
PANASONIC • 10
RUN
STATE
RESTORE
machine_counter_state stores the latest raw counters plus feeder_state and nozzle_state JSONB.
Node-RED starts → loads state into flow context → continues accurate delta calculation.
Notes: When Node-RED starts, the flow queries machine_counter_state and reloads the counters for each machine, feeder, and nozzle into the flow context.

## Slide 11
MPO | Manufacturing Performance Overview
PANASONIC • 11
02
DATA FOUNDATION
PostgreSQL combines relational schemas and JSONB for speed and flexibility.
From Raw Data to Operational Decisions

## Slide 12
POSTGRESQL DATA MODEL
Four Tables Form the Data Backbone
MPO | Manufacturing Performance Overview
PANASONIC • 12
MASTER
master_machines
Standardized machine catalog
FACT
production_reports
Central report history
DETAIL
feeder_logs
Feeder details by report
DETAIL
nozzle_logs
Nozzle details by report
STATE
machine_counter_state
Latest raw state
1 : N
1 : N
1 : N
1 : 1
Notes: The database separates master data, report history, feeder/nozzle details, and technical state. Clear relationships support fast reporting while preserving delta recovery after restart.

## Slide 13
CENTRAL FACT TABLE
production_reports: Historical Data
MPO | Manufacturing Performance Overview
PANASONIC • 13
OUTPUT
output_qty • board • module • pickup • mount
TIME
power on • production • stop • wait • error
QUALITY
pickup miss • mount miss • recognition • trouble
CYCLE
cycle_time_1 • cycle_time_2 • cycle_time_3
Analysis dimensions: machine • report date • MJS • product • lot • file

## Slide 14
DETAIL TABLES
Feeder and Nozzle Enable Root-Cause Analysis
MPO | Manufacturing Performance Overview
PANASONIC • 14
feeder_logs
Block code / serial / part / reel
Feeder & sub-feeder address
Pickup, mount, and miss counters
Multiple feeders per report
nozzle_logs
Head number / nozzle name
Nozzle & component address
Pickup, mount, and miss counters
Multiple nozzles per report
Outcome: prioritize the exact feeder, slot, reel, part, nozzle, or head to inspect.

## Slide 15
HYBRID STORAGE
Relational + JSONB: Fast and Flexible
MPO | Manufacturing Performance Overview
PANASONIC • 15
SQL
Relational columns
Core fields support stable filtering, joins, indexes, and reporting.
JSON
JSONB fields
Rare time stats, count stats, feeder state, and nozzle state remain flexible.
+
Foreign keys preserve relationships
ON DELETE CASCADE for details
Indexes by date, machine, MJS, lot, report, and address

## Slide 16
STORED PROCEDURE
One Centralized Write Point
MPO | Manufacturing Performance Overview
PANASONIC • 16
CALL
insert_full_production_report(payload JSONB)
01
Upsert Machine
02
Insert report
03
Insert feeders
04
Insert nozzles
05
Update counter state
Node-RED standardizes data; PostgreSQL handles relationships, writes, and state updates.
Notes: The stored procedure is the centralized write point: read machine_id, upsert master data, insert the report, process feeders/nozzles, and update machine_counter_state.

## Slide 17
MPO | Manufacturing Performance Overview
PANASONIC • 17
03
REPORTING APP
The application turns PostgreSQL data into dashboards, drill-downs, and exports.
From Raw Data to Operational Decisions

## Slide 18
APPLICATION ARCHITECTURE
Tech Stack Optimized for Web Reporting
MPO | Manufacturing Performance Overview
PANASONIC • 18
COLLECT
SFTP + Node-RED
STORE
PostgreSQL
BACKEND
.NET 9 + ASP.NET Core MVC
DATA
EF Core + Npgsql
FRONTEND
Razor + Bootstrap + Chart.js
DEPLOY
Docker containers
PostgreSQL → report services → MVC controllers → Razor pages → dashboard / table / export

## Slide 19
REPORT PORTFOLIO
Nine Views of the Same Data
MPO | Manufacturing Performance Overview
PANASONIC • 19
01
Overall Dashboard
02
Board Count
03
Production Report
04
By Part
05
By Feeder
06
By Nozzle
07
Cycle Time
08
Downtime
09
Total Pickup / Placement
Dashboard for direction → detailed reports for evidence and action.

## Slide 20
REAL APPLICATION • QUICK ACCESS
One-click access to the complete MPO reporting suite.
SCREEN 01 / 10
Notes: QUICK ACCESS: One-click access to the complete MPO reporting suite. Use this screen as evidence of the implemented workflow and explain the visible filters, results and export actions.

## Slide 21
REAL APPLICATION • OVERALL DASHBOARD
Management view combining output, equipment risk and downtime.
SCREEN 02 / 10
Notes: OVERALL DASHBOARD: Management view combining output, equipment risk and downtime. Use this screen as evidence of the implemented workflow and explain the visible filters, results and export actions.

## Slide 22
REAL APPLICATION • BOARD COUNT
Hourly output comparison by line and lane.
SCREEN 03 / 10
Notes: BOARD COUNT: Hourly output comparison by line and lane. Use this screen as evidence of the implemented workflow and explain the visible filters, results and export actions.

## Slide 23
REAL APPLICATION • PRODUCTION REPORT
Filtered production history with Excel export.
SCREEN 04 / 10
Notes: PRODUCTION REPORT: Filtered production history with Excel export. Use this screen as evidence of the implemented workflow and explain the visible filters, results and export actions.

## Slide 24
REAL APPLICATION • PICK-PLACEMENT BY PART
Trace misses and placement quality to part level.
SCREEN 05 / 10
Notes: PICK-PLACEMENT BY PART: Trace misses and placement quality to part level. Use this screen as evidence of the implemented workflow and explain the visible filters, results and export actions.

## Slide 25
REAL APPLICATION • PICK-PLACEMENT BY FEEDER
Identify feeder, slot and material-related losses.
SCREEN 06 / 10
Notes: PICK-PLACEMENT BY FEEDER: Identify feeder, slot and material-related losses. Use this screen as evidence of the implemented workflow and explain the visible filters, results and export actions.

## Slide 26
REAL APPLICATION • PICK-PLACEMENT BY NOZZLE
Prioritize nozzle and head maintenance from evidence.
SCREEN 07 / 10
Notes: PICK-PLACEMENT BY NOZZLE: Prioritize nozzle and head maintenance from evidence. Use this screen as evidence of the implemented workflow and explain the visible filters, results and export actions.

## Slide 27
REAL APPLICATION • CYCLE TIME REPORT
Compare cycle time by line, model and group.
SCREEN 08 / 10
Notes: CYCLE TIME REPORT: Compare cycle time by line, model and group. Use this screen as evidence of the implemented workflow and explain the visible filters, results and export actions.

## Slide 28
REAL APPLICATION • DOWNTIME REPORT
Measure error count and stop duration by line.
SCREEN 09 / 10
Notes: DOWNTIME REPORT: Measure error count and stop duration by line. Use this screen as evidence of the implemented workflow and explain the visible filters, results and export actions.

## Slide 29
REAL APPLICATION • TOTAL PICKUP / PLACEMENT
Compare pickup, placement and PPM across lines.
SCREEN 10 / 10
Notes: TOTAL PICKUP / PLACEMENT: Compare pickup, placement and PPM across lines. Use this screen as evidence of the implemented workflow and explain the visible filters, results and export actions.

## Slide 30
OVERALL DASHBOARD
Dashboard Prioritizes What Matters
MPO | Manufacturing Performance Overview
PANASONIC • 30
—
BOARD PRODUCED
Output by line
—
PPM
Relative quality
—
ERROR STOP
Error-stop duration
ACTION LISTS
Worst feeder
Worst nozzle
Pickup / Placement
Stop category
Compare by line and time range
Focus on top worst feeder / nozzle
Track pickup, placement, PPM, and stop time
KPI placeholder — actual values depend on filters.
Notes: The dashboard combines board produced, top worst feeder/nozzle, total pickup/placement, PPM, and error-stop time by line.

## Slide 31
PRODUCTION ANALYTICS
Three Reports Track Productivity
MPO | Manufacturing Performance Overview
PANASONIC • 31
01
Board Count
Output trends by line, lane, time, and model.
02
Production Report
Panel / pattern output by line, lane, model, and group.
03
Cycle Time
Evaluate cycle performance by line, model, and group.
Trend
Output comparison
Cycle distribution

## Slide 32
QUALITY ROOT-CAUSE
From Symptoms to the Source
MPO | Manufacturing Performance Overview
PANASONIC • 32
PART
At-risk part / scrap ratio
FEEDER
Table • slot • side • reel
NOZZLE
Head • nozzle • miss
Pickup + Placement + Miss groups + Scrap ratio
Same KPI logic, different analysis level.

## Slide 33
LOSS ANALYSIS
Downtime and PPM Guide Improvement
MPO | Manufacturing Performance Overview
PANASONIC • 33
DOWNTIME GROUPS
Pickup error
Recognition error
Single error stop
Trouble stop
Part exhaust
PPM
= Quality misses × 1,000,000
Total pickup / placement
Compare across lines
Prioritize the largest losses
Measure count and time
Bars illustrate layout only; they are not actual data.

## Slide 34
FILTER • TABLE • EXPORT
A Repeatable Analysis Experience
MPO | Manufacturing Performance Overview
PANASONIC • 34
01
FILTER
Date • shift • line • model • part
02
REVIEW
Detailed chart + table under the same criteria
03
REFINE
Pagination + adjustable column widths
04
EXPORT
All filtered results → Excel-compatible
Same filters → same evidence → faster sharing.

## Slide 35
MPO | Manufacturing Performance Overview
PANASONIC • 35
04
DEMO & SCOPE
A demonstration journey from overview to detailed evidence.
From Raw Data to Operational Decisions

## Slide 36
8-STEP DEMO
Demo Along the Decision Journey
MPO | Manufacturing Performance Overview
PANASONIC • 36
01
Open Dashboard
Overview of output, quality, and downtime
02
Select Time
Date range + shift → Apply
03
Board Produced
Compare output by line / lane
04
Worst equipment
Prioritize at-risk feeders and nozzles
05
Error Stop
Identify the largest stop category
06
Downtime Report
View count + time for each error
07
Drill-down
Filter feeder / nozzle by line and part
08
Export Excel
Share the exact filtered dataset
Core message: from “what happened?” to “where should we inspect?”
Notes: Demo journey: dashboard, time selection, Board Produced, top worst feeder/nozzle, Error Stop Time, Downtime Report, equipment drill-down, and Excel export.

## Slide 37
CURRENT SCOPE
Current Scope Confirmed
MPO | Manufacturing Performance Overview
PANASONIC • 37
IN SCOPE
Overall Dashboard + 8 detailed report groups
Report filters, pagination, and adjustable column widths
Excel-compatible export of filtered results
PostgreSQL retry, timeout, and cancellation handling
Antiforgery validation for unsafe MVC forms
NOT VERIFIED
Login / role-based access
Not included in the verified implementation.
The current user flow opens directly to the dashboard.

## Slide 38
MANAGEMENT TAKEAWAYS
Three Management Takeaways
MPO | Manufacturing Performance Overview
PANASONIC • 38
01
One Source of Truth
MPO centralizes machine, quality, and downtime data.
02
From KPIs to Root Causes
The dashboard guides; detailed reports verify.
03
Operationally Ready
Automated pipeline, restored state, and flexible export.
Raw machine data → operational evidence → focused action

## Slide 39
MPO | Manufacturing Performance Overview
PANASONIC • 39
THANK YOU
Q&A
Manufacturing Performance Overview
LNB → SFTP → Node-RED → PostgreSQL → Docker Web Portal
Accurate Data • Faster Analysis • Focused Action