## Slide 1
MPO
MANUFACTURING PERFORMANCE OVERVIEW
Manufacturing
Performance
Overview
2026
Notes: MPO is a web-based manufacturing performance reporting system that turns raw LNB machine data into dashboards and reports for daily operations.

## Slide 2
MPO
PIPELINE
DATABASE
REPORTS
02
EXECUTIVE SUMMARY
MPO Turns Machine Data into Action
MPO | Manufacturing Performance Overview
PANASONIC • 02
One automated flow unifies output, quality, and downtime—from .u01 files to the management dashboard.
01
Centralize
One unified reporting source for LNB machine data.
02
Analyze
Drill down by line, lane, machine, model, part, feeder, and nozzle.
03
Act
Identify at-risk equipment, investigate root causes, and export data.
Outcome: raw data becomes evidence for daily operations.
Notes: The dashboard highlights areas that need attention; detailed reports provide evidence for investigation.

## Slide 3
03
BUSINESS VALUE
Four Direct Operational Benefits
MPO | Manufacturing Performance Overview
PANASONIC • 03
01
One Data Source
Centralize production, quality, and downtime.
02
Reduce Manual Work
Eliminate multiple consolidation and file-reconciliation steps.
03
Faster Root-Cause Analysis
Trace issues from line to feeder, nozzle, or part.
04
Flexible Sharing
Export filtered results in an Excel-compatible format.
MPO
PIPELINE
DATABASE
REPORTS

## Slide 4
04
SYSTEM AT A GLANCE
One Architecture, One Data Flow
MPO | Manufacturing Performance Overview
PANASONIC • 04
01
LNB
.u01 raw data
02
SFTP
Secure transfer
03
Node-RED
Parse + delta
04
PostgreSQL
Store + state
05
Web MPO
Dashboard + export
AUTOMATED
No manual file handling is needed after data enters PostgreSQL.
MPO
PIPELINE
DATABASE
REPORTS
Notes: Overall flow: LNB raw data, SFTP, incoming folder, Node-RED Watch, parsing and delta calculation, PostgreSQL, ASP.NET Core, and the web frontend in Docker.

## Slide 5
05
CORE PROCESSING LOGIC
Delta Counters Preserve Actual Output
MPO | Manufacturing Performance Overview
PANASONIC • 05
DELTA
= Current counter − Previous counter
Applied to
Production • Time • Feeder • Nozzle
First Reading
Delta = Current
No previous state
Normal
Delta = Current − Previous
Record only the increment
Counter reset
Delta = Current
Current < Previous
Prevent double counting • Handle machine resets • Maintain cycle accuracy
MPO
PIPELINE
DATABASE
REPORTS
Notes: This is the most important point in the flow. Machines send cumulative values, while the system needs the actual increment for each period. Delta calculation prevents double counting and handles counter resets.

## Slide 6
MPO
PIPELINE
DATABASE
REPORTS
06
POSTGRESQL DATA MODEL
Database Structure
MPO | Manufacturing Performance Overview
PANASONIC • 06
MASTER
master_machines
Standardized machine catalog
FACT
production_reports
Central report history
DETAIL
feeder_logs
Feeder details by report
DETAIL
nozzle_logs
Nozzle details by report
STATE
machine_counter_state
Latest raw state
1 : N
1 : N
1 : N
1 : 1
Notes: The database separates master data, report history, feeder/nozzle details, and technical state. Clear relationships support fast reporting while preserving delta recovery after restart.

## Slide 7
MPO
PIPELINE
DATABASE
REPORTS
07
APPLICATION ARCHITECTURE
Tech Stack Optimized for Web Reporting
MPO | Manufacturing Performance Overview
PANASONIC • 07
COLLECT
SFTP + Node-RED
STORE
PostgreSQL
BACKEND
.NET 9 + ASP.NET Core MVC
DATA
EF Core + Npgsql
FRONTEND
Razor + Bootstrap + Chart.js
DEPLOY
Docker containers
PostgreSQL → Report services → MVC controllers → Razor pages → Dashboard / Table / Export

## Slide 8
08
REPORT PORTFOLIO
Dashboard
MPO | Manufacturing Performance Overview
PANASONIC • 08
01
Overall Dashboard
02
Board Count
03
Production Report
04
By Part
05
By Feeder
06
By Nozzle
07
Cycle Time
08
Downtime
09
Total Pickup / Placement
Dashboard for direction → detailed reports for evidence and action.
MPO
PIPELINE
DATABASE
REPORTS

## Slide 9
09
OVERALL DASHBOARD
Dashboard Prioritizes What Matters
MPO | Manufacturing Performance Overview
PANASONIC • 09
—
BOARD PRODUCED
Output by line
—
PPM
Relative quality
—
ERROR STOP
Error-stop duration
ACTION LISTS
Worst feeder
Worst nozzle
Board count
Stop time
Compare by line and time range
Focus on top worst feeder / nozzle
Track pickup, placement, PPM, and stop time
KPI placeholder — actual values depend on filters.
MPO
PIPELINE
DATABASE
REPORTS
Notes: The dashboard combines board produced, top worst feeder/nozzle, total pickup/placement, PPM, and error-stop time by line.

## Slide 10
10
PRODUCTION ANALYTICS
Three Reports Track Productivity
MPO | Manufacturing Performance Overview
PANASONIC • 10
01
Board Count
Output trends by line, lane, time, and model.
02
Production Report
Panel / pattern output by line, lane, model, and group.
03
Cycle Time
Evaluate cycle performance by line, model, and group.
Trend
Output comparison
Cycle distribution
MPO
PIPELINE
DATABASE
REPORTS

## Slide 11
11
QUALITY ROOT-CAUSE
From Symptoms to the Source
MPO | Manufacturing Performance Overview
PANASONIC • 11
PART
At-risk part / scrap ratio
FEEDER
Table • slot • side • reel
NOZZLE
Head • nozzle • miss
Pickup + Placement + Miss groups + Scrap ratio
Same KPI logic, different analysis level.
MPO
PIPELINE
DATABASE
REPORTS

## Slide 12
12
LOSS ANALYSIS
Downtime and PPM Guide Improvement
MPO | Manufacturing Performance Overview
PANASONIC • 12
DOWNTIME GROUPS
Pickup error
Recognition error
Single error stop
Trouble stop
Part exhaust
PPM
= Quality misses × 1,000,000
Total pickup / placement
Compare across lines
Prioritize the largest losses
Measure count and time
Bars illustrate layout only; they are not actual data.
MPO
PIPELINE
DATABASE
REPORTS

## Slide 13
13
MPO | Manufacturing Performance Overview
PANASONIC • 13
THANK YOU
Q&A
Manufacturing Performance Overview
LNB → SFTP → Node-RED → PostgreSQL → Docker Web Portal
Accurate Data • Faster Analysis • Focused Action